## Slide 1: Two Planets: Challenges of Living on Earth & Mars
Frank H. Shu1 & HX Team (formed 2009)2
1ASTRON Solutions Corporation
2 August 2017
Wu Chien Shiung Science Camp
2ASIAA: P. Ho, R. Krasnopolsky, R. E. Taam, T. S. Wei, S. J. Zheng; IoC; F. T. Luo, H. F. Tseng;
NTHU: N. H. Tai, P. F. Cheng, D. S. H. Wong; ITRI: S. K. Wu; CityU: C. T. Liu; UMich, R.T. Yang; S. CA: F. S. Model, S. Chien
Notes: 1M. J. Cai, F. T. Luo, P. T. P. Ho, R. E. Taam, Y. D. Huang. T. S. Wei, K. H. Chien, S. K. Wu, S. Chien, N. H. Dai, S. J. Zheng

## Slide 2: Outline of Talk
Motivations for colonizing Mars
  Challenges to survival on Earth
  Challenges to survival on Mars
Getting to Mars (& back)
  Hohmann transfer orbit
  Chemical and nuclear rocket propulsion
Living and working on Mars
  Water, oxygen, and thorium
  Making methane fuel
  Building a high-tech carbon-based economy
  Transforming Martian soil from sterile/toxic to fertile
Lessons for Earth from thinking about Mars (and vice-versa)
  Using biochar to reverse climate change
  Making nuclear energy Safe, Sustainable, Secure, $uperior* (may skip)
ESA
Notes: A climate scientist and a climate skeptic walk into a bar. The skeptic says to the bartender, “What’s your strongest drink?” The bar tender brings out a bottle and says: “This one is 97% alcohol but it’ll cost you more.” The skeptic slams his fist on the bar, yells, “I’m not paying,” and storms out. The scientist turns to the bartender and says: "That's the trouble with these guys; you show them the proof, and they still don't buy it.”

## Slide 3
  Challenges to survival on Earth
Notes: A climate scientist and a climate skeptic walk into a bar. The skeptic says to the bartender, “What’s your strongest drink?” The bar tender brings out a bottle and says: “This one is 97% alcohol but it’ll cost you more.” The skeptic slams his fist on the bar, yells, “I’m not paying,” and storms out. The scientist turns to the bartender and says: "That's the trouble with these guys; you show them the proof, and they still don't buy it.”

## Slide 4: Antarctica Ice Core Data Milankovic cycle, amplification, & positive feedback
In its present configuration, Earth is on the brink of instability, with small forcings leading to large amplification & feedback that produce climate “phase change.”

## Slide 5: Mean Temp Rise & Arctic Death Spiral
CH4 Nov 2002
CH4 Jan 2014
Since industrial revolution, mean surface temp  1.2 oC
Polar regions most sensitive;
glacial ice on a death spiral.
Switching from coal to nat
gas not a solution:
  Only 50% better if no leaks
  If leaks, CH4 85x worse for 20 yr, 25x for 100 yr
Fracking for nat gas & drilling
for off-shore methane hydrate
(“combustibe ice”): potentially
disastrous for leakage of CH4
Reliance on nat gas to back up solar/wind: an unrealisic “solution” to a dire problem.
Time to move to Mars?
NASA GISS

## Slide 6: Challenges to Survival on Mars (Useful exercise to appreciate Earth)
Low surface temperature and pressure
Solution: pressurized & heated habitats
Low surface gravity
Solution: wear weighted suits
No magnetic field to shield against galactic cosmic rays
Solution: live inside – underground shielding (> 4 m rock)
Travel or work outside – superconducting magnetic shields
High per capita needs for energy/materials
Solution: thorium molten-salt breeder-reactor

## Slide 7: Lower Martian Gravity Twin paradox: Earth twin cannot dunk, Mars twin can

## Slide 8: Exposure to Galactic Cosmic Rays Leads to Brain Damage Compression of Earth magnetosphere by solar storm in 2016 (Mars has no magnetic field today – planetary dynamo has died)
11 RE  4 RE
If Earth with a field with a
strength of 65 microtesla
at a pole can provide enough
protection for a surface with
radius RE, what is the zone
of protection afforded by a
supercoducting magnet of
the Large Hadron Collider
with a field strength of 8.33
Tesla at a pole? (mass of
equipment = 35 tonne)
Answer: about 10 m.
In an equatorial belt betw
7 m and 10 m, the field
strength is similar to a
“closed” MRI machine.
Tata Institute of Fundamental Research Cosmic Ray Laboratory

## Slide 9: Ice and Dry Ice on Mars Water & Dense Carbon Dioxide Available to Melt, Clean, & Transform
Ordinary or advanced
electrolysis to split water:
H2O + elec H2 + ½ O2
Sabatier reaction to make
methane exothermically:
4H2+CO2  CH4 + 2H2O
+ heat
Net reaction,
CO2+2H2OCH4+2O2,
requires energy input

## Slide 10: Sustaining Life for Months w/o Fresh Water & Air
Problem faced by submarine crews (~ 140)
  Solution: nuclear reactor w P ≈4x3 MWt*
  Enriched U fuel (US & UK > 90% U-235)
  Water cooled & moderated (PWR)
  Fresh water by distilling seawater
  Oxygen by dissociating H2O (torpedo away H2); CO2 captured & disposed
  * Fdu = (½Cdρu2A)u = 0.001(1000 kg m-3)(12.5 m/s)3π(12.5 m)2 ≈ 1 MW
With professionally trained operators, completely safe
  Automatic shutdown: if lose coolant, also lose moderator
  Decay heat? (0 hr: 6.5% P; 1 hr: 0.6%); not a problem at low P
US exported LWR technology ( PWR & BWR) to rest of world, except for mavericks who wanted fuel that can be natural U (0.7% U-235, 99.3% U-238)
  Canada: heavy water (CANDU) reactors (D2O not H2O, which absorbs n)
  USSR: graphite moderated, water cooled; only accident to have runaway chain reaction (Chernobyl)
Defence Industry Daily

## Slide 11: Energy is the Driver of Matter Transformation and Defines the Limits of a Developed Society Deep Meaning of E = mc2

## Slide 12: The S-Diagram of Energy
J/L
J/kg
Compactness of equipment
Duration of use
Sun and wind stronger on Earth than Mars. Earth headed for climate catastrophe w/o new nuclear (Caldeira, Emmanuel, Hansen, Wigley (2016)
Coal loses to wind/gas b/c of
renewable mandates, need
to scrub noxious emissions,
& inefficient steam turbines
Notes: Cheapest way to produce H2 is via coal gasification:
2C (s) + O2 (g)  2CO (g),
CO (g) + H2O (g)  H2 (g) + CO2 (g);
Then combine H2 (g) with C (s) to make liquid hydrocarbons.

## Slide 13
Breaking the Paradigm of Turbine Electricity Generation
GE Supercritical CO2 (sCO2) Turbine: Sunrotor 10 MWe
In normal gas turbine, CO2 in combusted fuel is a gas. In sCO2 turbine, CO2 is at T > 400 oC & P > 100 bar high enough to lose distinction betw gases & liquids. I.e., sCO2 can expand like a gas to create flowing fluid with almost density of a liquid. (Imagine augmented power of turbine on jet plane expelling exhaust 100x denser than air.) Compact coupling of molten salt heat & sCO2 turbine. Polar caps of Mars contain frozen CO2 (dry ice, the ideal dense starting state for sCO2).

## Slide 14: Myth: Nuclear Power Is Expensive w Negative Learning Curve Lovering, Yip, Nordhaus (2016)
USA
France
Japan
Korea
Solar PV (res)
Solar PV (utl)
Straight-line on log-log plot  power law
To avoid “cost-escalation,”
must achieve safety by
physics, not by engineered “defense in depth”
Large-scale release of
radioactivity to environment
& theft of weapons-grade
nuclear materials should be
essentially physically
Impossible.
Burning U-235 is
unsustainable and not
suitable for Mars in the
long run.
On all these points, thorium
Is a better choice

## Slide 15: Thorium on Mars Th-232  Pb-208 by 4 beta & 6 alpha, then a gamma: t1/2= 14 Gyr
www.mars.jpl.nasa.gov/odyssey
Nat Th is pure Th-232, 4x more abundant than U, no enrichment needed

## Slide 16: Basics of Nuclear Energy
Fission vs Fusion: n vs charged particles

## Slide 17: Nuclear Fission
Fissile, even p, odd n: n + + 2 or 3 n (1 for chain reaction)
  U-235 (0.7% of natural U)
  Pu-239 breed by adding excess n to fertile U-238 (99.3% U)
  U-233 breed by adding excess n to fertile Th-232 (100% Th)
FPs
233U(n,FP)FP
235U(n,FP)FP
239Pu(n,FP)FP
Pu-239
U-233
U-235
# n per fission event
n energy (eV)
n energy (eV)
σ (barn)
σ (barn)
σ (barn)
n energy (eV)
n energy (eV)
1E3
1E0
1E0
1E6
1E-3
4.0
3.0
2.0
1.0
1E0
1E0
1E3
1E6
1E3
1E6
1E3
1E0
1E-3
1E3
1E0
1E3
1E6
1E-3
1E0
1E3
Pre-WW2 discoveries:
Fermi: bombard U w n,
results depend on bench
Hahn: discover Ba (Z=56)
Meitner & Frish: U fission
Bohr: U-235 = fissile
Szilard & Fermi: crit mass
Research classified

## Slide 18: U-238/Pu-239 Breeder Fuel Cycle
Number of protons Z
Number of neutrons N
Capture of n w gamma emission increases N (red arrows)
Beta decay turns n into p (blue arrows)
Beta decay violates parity conservation (post-war YCN, LTD, & WCS)
Alpha decay drops N by 2 and Z by 2 (black arrows)
U-235: t1/2 = 0.7 Gyr, 0.7% of UO2, UO3 water soluble, UF4 s or l, UF6 g
U-238: t1/2 = 4.5 Gyr, 99.3% of UO2, centrifuge UF6 to 3-20% U-235 for LWRs
Pu-239: t1/2 = 24 kyr, large fission σ, but 40%  Pu-240, only fast breeder possible
Pu-240: spontaneous fission, deterrent to weapons proliferation

## Slide 19: Th-232/U-233 Breeder Fuel Cycle
Th-232: t1/2 = 14 Gyr, 100% nat Th, 4x abundance of U in crust
U-233: large fission σ, 8% branching  U-234, thermal breeding OK
n-caps  U-235 w large fission σ; n-caps dead-end U-236 or Pu-238
Weapons deterrent: 232Th(n,2n)231Th(β-)231Pa(n,γ)232Pa(β-)232U, fast n
Number of protons Z
Number of neutrons N
?
Fermi-Wigner debate
(n,2n)

## Slide 20: Getting to Mars
    Reusable chemical rockets to low earth orbit (LEO)
    Fission fragment shuttle from LEO to Mars Orbit
    Difficult descent from Mars orbit to surface
    Thorium molten-salt breeder reactors for use on surface

## Slide 21: Getting to Mars (and Back) Conventional Approach: Hohmann Transfer Orbit
Approximate Earth and Mars
to have circular orbits about Sun
Boost spaceship from LEO into
circular orbit of Earth around Sun
Add 3 km/s to the circular orbit
to put spaceship into elliptical
Hohmann transfer orbit
After 259 days, spaceship at
aphelion & Mars circle; time
launch so that Mars will be there
Add 2.5 km/s to the Hohmann
transfer orbit to put spaceship
into Mars’s circular orbit
Have 459 days to explore surface
of Mars before begin 259 d trip
back to Earth & reentry by drag
Earth orbits Sun 30 km/s
orbits Sun 24 km/s
1 AU
1.52 AU
clowder.net
SpaceX (Blue Origin, Virgin Galactic) innovation:
reuseable rockets

## Slide 22: Unconventional Approach
  Rocket science: d(Mv) = -(dM)(Δv-v)  added v = Δv ln(Mi/Mf)
  Δv for fission fragments 13,000 km/s ~ 3000x chemical propellents
  Recycle organic waste & water, only ejecta FPs: v ≈ Δv(MFP/Mf)
  Not Hohmann: v accumulated gradually rather than impulsively
  Small payloads: potentially possible to get to Mars in 2 weeks (!) people
  Large paylods: tangential thrust w ½ FPs (33.2 N)  2.24 yr for trip from Earth to Mars, & each tonne paylod to Mars needs 1 MWt from 2F-MSR
  Payload/fuel ratio ≈ 1000
  On Mars arrival, parachute (?) 2F-MSR (CFRC pipes) & 233UF4 onto surface
  Task is easy; most of weight is in fluoride salts, which cannot be damaged
Example: ISS (420 t) needs 420 MWt 2F-MSR on-board w sterile
blanket salt (not breeder) to give excess neutrons for Ni-on-
Glass guide-tube ion-propulsion

## Slide 23: More Detailed Design
Earth to Mars travel time = 2.24 yr (after LEO  Lunar L1  L2)
Mean acceleration = 8 μg; artificial gravity (~ 2 min rot period)
Mass budget = 420 t = 113 t carbon composite structure + 60 t H2O (shielding against γ)+ 105 t magnetic shielding (against GCR) + 111 t MSR & FFRE+ 0.72 kg U-233 fuel to propel spaceship w 0.23 t left for 10 yr use on Mars at 60 MWt of power + 28 t food + 2.28 t crew*
    MSR radiator 100 m x 37 m x 0.01 m (74 t including blanket salt at 1000K)
    FFRE radiator (37 t including blanket salt at 1000 K)
*US DOE has 1 tonne 233U; downblending b/c nuclear proliferation concerns
NASA/TM-2005-213559
except fission not fusion
www.cbsnews.com
SpaceX launches comsat

## Slide 24: Carbon Fiber Fuel Tanks & Reactor Core Elon Musk, Making Humans a Multi-Planetary Species (SpaceX, 2016) Frank H. Shu, Two-Fluid Molten Salt Reactor (US Patent 20120051481) A1)
SpaceX
SpaceX
HX
Idea of using carbon fiber as strong lightweight
construction material not new, e.g., tennis racquets,
bicycles, SMA, Boeing 787, Lamborghini SE, ALMA
However, carbon fibers weaved Into a cloth are porous
Must seal to hold liquids, e.g., rocket fuel or molten salt
Such graphitic materials have virtue of being
  strong at high temperatures
  not corroded by molten fluoride or chloride salts
High-T use in space/Mars does not need Al2O3 cladding
HX
Nuclear-grade graphite
immersed in 900 oC
molten fluoride salt

## Slide 25: Carbon is the Future in Construction & Electronics
Each carbon atom in graphite double (sigma) bonded in planar
direction to 3 other carbons. Sigma covalent bonds:
  very strong
  not broken by any reactant other than oxygen (at edges)
In an oxygen-free environment (e.g., immersed under anoxic
molten salt), reactor-grade graphite resistant to attack by any
other element in the periodic table (e.g., fission products)
Since C has 4 valence electrons, sigma-bonding to 3 other C’s
uses up only 3 valence electrons; 4th electron free to
  form out-of-plane bond to other atoms (e.g., H), or
  roam through lattice (conductor or semi-conductor,
  depending on impurities occurring naturally or doped)
Binding across planes in graphite is weak (van der Waal forces);
can peel one plane from others using scotch tape (2010 Nobel)
Graphene = single sheet of graphite (2016 cost: US$100/g)
Graphene rolled up into a cylinder = C-nanotube
C-nanotubes strong & light, good for construction & electronics
C-nanontube rolled up in 3rd dimension = buckyball or fullerene
Diamond w each C double-bonded w 4C = strongest 3-D structure
Lacking free O2, Mars may be better for making double-bonded C

## Slide 26: Descent of Rovers to Martian Surface
Spirit & Opportunity rovers
solar powered
Curiousity rover: nuclear powered (RTG)
NASA
NASA
Taiwan to participate in building next-generation rover

## Slide 27: Tsiolkovksy & Artsutanov’s (1959) Dream - Space Elevator Cable of C-nanotubes tethered at Mars synchronous orbit (24.62 hr) Cf. Phobos orbit = 7.66 hr , Deimos orbit = 30.35 hr (all sidereal)
Art credit: Caltech
Mars synchronous orbit at GM/rs3 = ω2 where ω =2π/24.62 hr at rs=xsr0 w xs=6.025 & r0=3390 km
Equatorial eff grav field: geff = -GM/r2 + ω2r = g0(-x-2+xs-3x) w g0 = GM/r02 = 0.38 g & x = r/r0.
Descent/ascent time: maybe day or two
Cable tension balances grav: d(σA) + geffρAdr = 0
If σ = const, ln(A/A0)=(g0ρr0/σ)[1-x-1+(xs-3/2)(1-x2)]
At x = xs: ln(As/A0) = 0.7533(g0ρr0/σ)
fat @ rs, skinny @ r0; inverted Taipei 101
Example: If σ = g0ρr0 = 20 GPa (1 atm = 0.1 Mpa) & ρ = 1600 kg/m3 (C-nanotube), then ln(As/A0) = 0.7533 or As/A0 = 2.124. C-nanotube theoretical breaking strength σ ≈ 300 Gpa.✓ However, C-nanotube may unzip w single defect (Ding et al. 2016). Cable mass (r0 to rs) = 9.399ρA0r0 = 1.6x109 kg if A0 = π(0.1m)2. Cost per kg?
 Elevator = tuning-fork w tines 200 km N & S of equator?
Think of tall bamboo w superstrong fibers
.
Phobos
from
Mars
Surveyor

## Slide 28: Living & Working on Mars
Take technological advantage of the lower gravity & extreme
cold to create a sustainable space-faring society where:
Free oxygen to corrode metals does not exist, relaxing an important constraint on the production of high-Th alloys
Low ambient Ta and high Th yields greater eff for heat engines based on sCO2 turbines; ideally, eff = (Th – Ta)/Ta
No free oxygen implies no free burning of chemical fuels
A thorium economy can provide abundant clean energy
Natural existence of CO2 & H2O at solid densities & no free O2 imply easier manufacture of CH4 & O2 (rocket fuel)
Favorable environment for development of high-tech carbon industry can justify colonization investment
Biochar (low-end C) can make dead planet bloom with life

## Slide 29
Herbert’s Dream in “Dune”:
Transforming a Desert Planet
Heat biomass in absence of O2 to produces charcoal = biochar
Add biochar to carbon-depleted soils to enhance crop productivity
Hood-Nowatny (2016): 75% increase in soil productivity in tropical & temperate zones
Circular economy: biomassbiocharmore arable land for growing biomass, …

## Slide 30: What is Biochar? Carbonized Biomass. How can it be cleanly & quickly manufactured? Supertorrefaction Submerge biomass under molten salt at 300 to 550 oC for 10 to 1 min Reaction rate at constant P & T proportional to exp(-ΔG/RT) w |ΔG| ~ R(104 K)
STR Patents: TW, CN, USA, RUS, CAN, UK, FR, DE, JP, IN, BR, AU
YouTube video

## Slide 31
0602-550550 C for 1 min followed by washing with 2N nitric acid and water
Biochar & Activated C from Leucaena at 550 oC in 1 min BET CO2 = 414 m2/g (cf. Graphene 2600 m2/g)
Cells
Microfibrils

## Slide 32
0602-550550 C for 1 min followed by washing with 2N nitric acid and water
Perchlorates in Martian Soil
Phoenix Mars polar lander found Martian soil
to contain by weight 0.6% perchlorate salt in
proportions Ca(ClO4)2:Mg(ClO4)2 = 60:40
Perchlorate salt, a powerful oxidant, is toxic to
beneficial soil bacteria and to humans
Fortunately, Ca(ClO4)2 & Mg(ClO4)2 are highly soluble in water:
  Can filter them w activated-C/biochar
  Molten salt 300 oC < T < 400 oC melt &
  decompose perchlorates:
  Melt: Ca(ClO4)2 + heat  Ca++ + 2ClO4-
  Decompose: 2ClO4- + heat  2Cl- + 4O2
  Wet CaCl2 and MgCl2 can keep down dust;
  but release of O2 needs regulation on Mars
  (Oxygen now in rust or rocks or H2O or CO2)
HX
NASA JPL/Caltech-UAriz

## Slide 33: Lessons for Earth from Thinking about Mars (and vice-versa)

## Slide 34: Reversing Climate Change on Earth
Flatten curve to 450 ppm by 2050
With New Nuclear Energy + Renewables (STR, biofuel, hydro, wind, solar, geo)
*
*
*
*
*
*
*
*
*
*
*
*
*
*
Keeling Curve for CO2 Concentration at Mauna Loa
Pledged INDCs
*
*
Full record ending 30 July 2017
Safe
Beyond 2050, reduce CO2 by 2 ppm per year w biochar to recover desertified lands. Circular/sustainable economy: waste  resource by leveraging nuclear energy = 2x106 chemical
1960 1970 1980 1990 2000 2010 2020 2030 2040 2050
Business as usual:
Before end of century: 3-4 oC
Asia-Pacific: 6 oC
1000-yr timescale: 60 m sea rise
CO2 Concentration (ppm)
Notes: IEA: T$84.5 (all sectors) by 2040

## Slide 35
Patented Improvement: 2F-MSBR FHS Patents: USA, CN, RUS, JP, FR, GB, DE, SE
Novel Features
Carbon Composite Materials to Resist MS Corrosion
Large Pool to Prevent Weaponization of Bred U-233
Making Nuclear Energy
Safe, Sustainable, Secure, & $uperior
ORNL
YouTube Videos

## Slide 36: Two-Fluid (fuel & coolant) MSBR (ORNL) = LFTR (Sorensen) Solves problems of disposing LWR waste & sustainability of nuc option
LWR used fuel Th-232 Blanket ThF4
  U-238, U-235
  Pu/actinides
  Fission prod’s
Th-232
300 yr
Ground
IFR or LFR
or TWR
Graphite
Core
Carrier:
On Earth:
Pu/An in core converts Th-232 into U-233
On Mars:
U-233 in core gives breeder 2F-MSBR
UF4 (pool) FV UF4 (core)
233U & 232U from (n,γ) & (n,2n)
7LiF/BeF2 or NaF/BeF2
FPs
nuc medicine, nuc batteries (Pu-238, Sr-90)
Regulated
Use (Wiki)
232Th(n,γ)
233Th(β−)
233Pa(β−)
233U

## Slide 37: Modified Design - *Differences from ORNL Assembly of CFRC Pipes* Carrying Fuel Salt in Large Pool* of Blanket Salt w Floating Graphite Balls* that Define a Spherical Core
Core + pool = Tube & shell HX: most efficient ΔQfΔQb
Tf and Tb controlled
by how hard one
pumps 2 fluids
Decay heat flows
to pool to run pumps (4 fuel salt,
4 blanket salt)
Station blackout:
keep running at
least 1 + 1 pumps
to cool fuel salt
Loss of coolant
accident:
Lose absorber ThF4
& moderator as
G balls drop to
floor of pool
Freeze plugs open,
drain fuel salt into
passively cooled
dump tanks
Dump tanks dilute
fuel with enough
sterile salt so
mixture freezes if
spilled from tank
FPs never escape
into environment

## Slide 38: Neutronics
Scattering of n off nuclei 9x, 12x, 19x, 23x heavier than itself
<Δv> & <ΔvΔv> << v & vv Fokker-Planck in speed space (like globular-
cluster dynamics, cosmic-ray acceleration, Black-Scholes stock pricing)
Alternative to MCNT: Forsberg & Greenspan (2003), Mathieu et al. (2005)
SED of Grape reactor (D = 2.4 m) very different from SED of LWRs
ξ3/2ϕ(ξ)
ξ = ε/kT (kT = 0.1 eV)
Critical mass for U-233 = 104 kg
Breeding ratio depends on how
clean salt is of FP
Critical mass for Pu-239 = 30 kg
Conversion ratio > 0.6 (0.8-0.9?)
Not yet enough LWR “waste”
to build required fleet of 2F-MSBRs
to halt & reverse climate change
1
100
102
104
106
108
10-2
Initiation
of most 
of fission
reactions
Responsible
for generating
weapons
deterrent 
Notes: 1

## Slide 39: Shippingport Reactor Vessel (236 MWt) HEU LWR: U-233 seed, Th-232 blanket, Breeding ratio = 1.01 2F-MSBR w cleaner, safer, more compact system should do better

## Slide 40: Thorium Breeder Reactors for Earth
Sustainable: Proven Th reserves enough to supply 100% of world energy needs for > 400 yr, long enough to develop fusion
  No “waste” except FPs that decay to background levels in 300 yr
  Industrial processing: Fluoride volatility, vacuum distillation (easy on Moon or Mars)
Safe: Runs without operator decisions except for advance scram
Secure: Always U-232 mixed w U-233 in 2-fluid MSBR; optional Pu-239Pu-240 (esp. MSBRs w more thermal spectrum)
$uperior: sCO2 turbine rather than steam
  Excellent coupling to molten salt
  Very compact equipment
  High thermal efficiency (> 50%)
  Development paid by solar thermal
Notes: v = Δvln(Mi/Mf)

## Slide 41: The Path Forward on Earth & Mars
Path forward driven by international interest to colonize Mars
  Transparency to open up understanding of 2-fluid MSBRs vs. alt’s
  Lack of transparency is what led to arms race & illogical fear of nuclear energy w resultant threat to the survival of civilization
  CN, RUS, JP, EU intend to establish lunar base; USA contribution: nuclear reactor? (Kirk Sorensen before 2001 for Moon)
  RTG experience: Voyager/Galileo/Cassini/Pluto (Pu-238 decay)
  Class 104(c) research reactor where < 50% of power/products are sold may fast-track NRC regulation (Rod Adams)
Spin-off applications for Th-2F-MSBR: scaled-up version to save civilization on Earth from climate change
Notes: v = Δvln(Mi/Mf)

## Slide 42: Thank You Everyone!
Astron

## Slide 43: Energy Mix Since Scientific Enlightenment Bill Gates: “We need an energy miracle” (Atlantic 2015)
Coal
Nat Gas
Oil
Hydro
Nuc
Biomass
New Renew
Use of coal started industrial revolution in mid-18th century
End of slavery in mid-19th century (England 1830 & America 1864)
In 20th century, wars (colonial, WW1, WW2) fought over nat resources in africa, middle east, far east, & europe, but MAD prevented WW3
In 21st century, burning of FFs  global warming & related conflicts

## Slide 44: Policy of Cheap Oil Allows Economic Globalization; Lack of Social Cohesion Drives Income Inequality
Uneven effects of climate change on rich & poor
Can the threats of climate change catalyze a new social compact?
Or should we start over on Mars?
Answer to both may be synergistic
Map of GINI index: 0 = complete equality; 1 = complete inequality